## Slide 1
DSC, Latur Department of Physics
M.Sc. S. Y (Sem-IV).
Lecture- 16
Losses, dispersion in fibers, sources and detectors for optical fibers
Presented By
Mr. L. H. Kathwate
M.Sc. B.Ed., NET, SET, GATE

## Slide 2
What is Optical fiber?
An optical fiber is a very thin and flexible medium, having a cylindrical shape consisting of three section core, cladding and jacket.

## Slide 4
Distortion, is a result of communication in which the original intended meaning of a massage is replaced with different interpretation as the receiver.

## Slide 5
What is attenuation in optic fiber?
In an optical fiber, whenever a signal is transmitted there is a loss of its power and hence its output intensity decreases with respective to the distance travelled. This loss in intensity of light beam through a fiber is called attenuation
Or
Simply attenuation in optical fibers means loss of optical power in the fiber itself.

## Slide 6
Mathematically, the loss is expressed as;
(2.1)
where, - Out-put power; - Amount of power coupled into the fiber; - Fiber attenuation in dB/km.
Attenuation loss per unit length is given by;
(2.2)
Hence, attenuation in the fiber is defined as the ratio of the optical power output obtained from a fiber of length L to the optical power fed to the input of the fiber.

## Slide 7
This loss may arise from different sources such as;
Material absorption,
Scattering,
Mode coupling,
Leaky modes,
Bending of the fiber,
Radiation induced attenuation,
Defective construction losses,
Transmission losses, and
Core and cladding losses.

## Slide 8
Losses are expressed in decibels per kilometer (dB/km).
In the case of an ideal fiber input and out power is equal hence there is no loss of optical power. In other words, for an ideal fiber, the attenuation is zero.
But practically this is not possible, because all fibers have a certain amount of loss, from microscopic bubbles and actual attenuation due to dielectric hysteresis, etc.
At the operating wavelength 1550nm the normal range of attenuation in single mode fiber at the 0.154 dB/km and for plastic fiber at same wavelength attenuation is 10 dB/m.

## Slide 9
Material or impurity losses
During the fabrication of various types of fibers, in order to modify the refractive index we use we dopants in silica such as;
Germanium Dioxide-
Phosphorus Pentoxide- and
Boron Trooxide etc.

## Slide 10
While produces strong absorption peaks at,
produces the same at .
However, in both these case absorption-tails extend below .
That is why boron and phosphorous based doping are not used in the low loss, single mode fiber.

## Slide 11
Experiments have shown that the loss increases considerably when the operating wavelength is beyond 1.55 um. This is an inherent property of all silica based Fibers. This is perhaps due to vibrational resonance of the silica tetrahedron molecules. Its contribution at different operating wavelengths is given in Table 2.1. This loss is due to interaction light with molecular structure of the material and also due to material impurities.

## Slide 12
Rayleigh scattering loss

## Slide 13
The glass, which is used in the fabrication of fibers, has many microscopic inhomogeneities and material density fluctuations of the silica material contents. As a result, a portion of light passing through the glass fiber gets scattered. This phenomenon is called "Rayleigh scattering".

## Slide 14
These inhomogeneities are frozen into the silica matrix when the fiber is formed and depend on the glass-forming temperature. Lower the glass-forming temperature lower is the density fluctuation and hence scattering.
As stated earlier it is also a function of glass-forming temperature. Attenuation due to this is quite complex in nature.

## Slide 15
The scattering loss due to density fluctuation only can be expressed as;
(2.3)
where - operating wavelength; -Boltzmann constant; -Fictive temperature (temperature at which the density fluctuations frozen into the glass as it solidifies); -Isothermal compressibility of the material. Above relation shows that scattering losses varies as .