## Slide 1
Interrupts

## Slide 2
Interrupts



Interrupt Basics
The Shared-Data Problem
Interrupt Latency
2

## Slide 3
Interrupt Basics


Interrupts are triggered when certain events occur in the hardware.
 e.g. when a serial chip has sent data to a microprocessor and wants it to read it from its pin, it sends an interrupt to the processor, usually by sending a signal to one of the processor’s IRQ (interrupt request) pins.
On receiving an interrupt, the microprocessor stops its current execution, saves the address of the next instruction on the stack and jumps to an interrupt service routine (ISR) or interrupt handler.
3

## Slide 4
Interrupt Basics (cont.)


The ISR is basically a subroutine written by the user to perform certain operations to handle the interrupt with a RETURN instruction at the end. It is a good practice to save register state and reset the interrupt in ISRs.
ISRs are similar to a CALL except that the call to the ISR is automatically made.
4

## Slide 5
Interrupt Example
Task Code ISR
...
MOVE R1, R7
MUL R1, 5
ADD R1, R2 ...
DIV R1, 2 ...
JCOND ZERO, END ;ISR code comes here SUBTRACT R1, R3 ...
... ...
...
END: MOVE R7, R1 RETURN(I) ...
...
5

## Slide 6
Interrupts and State
Saving and Restoring the Context





As the above code demonstrated, the task code has no idea of the changes taking place in registers like R1 or R2 in the ISR.
Hence if R1 is modified by the ISR, we might get an incorrect final result.
Due to limited number of registers, the ISRs and task codes usually have to work with same registers.
To solve this problem it is common practice to save the register contents onto the stack (saving the context) and restoring them at the end of the ISR (restoring the context). This is mandatory to prevent any bugs from appearing due to interrupts
6

## Slide 7
Interrupt Example (Push/Pop)
Task Code ISR
...
MOVE R1, R7
MUL R1, 5 PUSH R1
ADD R1, R2 PUSH R2
DIV R1, 2 ...
JCOND ZERO, END ;ISR code comes here SUBTRACT R1, R3 ...
... POP R2
... POP R1
END: MOVE R7, R1 RETURN(I) ...
...
7

## Slide 8
Disabling Interrupts




Most microprocessors allow programs to disable interrupts.
In most cases the program can select which interrupts to disable during critical operations and which to keep enabled by writing corresponding values into a special register. Nonmaskable interrupts however cannot be disabled and are normally used to indicate power failures or other serious event.
Certain processors assign priorities to interrupts, allowing programs to specify a threshold priority so that only interrupts having higher priorities than the threshold are enabled and the ones below it are disabled.
8

## Slide 9
The Shared-Data Problem
In many cases the ISRs need to communicate with the task codes through shared variables:
Void main (void)
{
Static int iTemperatures[2]:
Void interrupt vReadTemperatures (void)
int iTEmp0, iTemp1:
{
}
iTemperatures[0] = !! Read in value from hardware iTemperatures[1] = !! Read in value from hardware
while(TRUE)
{
iTemp0 = iTemperatures[0];
iTemp1 = iTemperatures[1];
if (iTemp0 != iTemp1)
!!Set off howling alarm;
}
}
9

## Slide 10
Shared Data





The code continuously monitors two temperatures and sets off an alarm if they are different.
An ISR reads the temperatures from the hardware. The interrupt might be invoked through a timer or through the temperature sensing hardware itself. Now, consider that the temperatures are 70 degrees and an interrupt occurs after iTemp0 = iTemperatures[0] is executed.
The temperatures now become 75 degrees. Hence on returning from ISR, iTemp1 will be assigned 75 and an alarm will be set off even though the temperatures were the same.
10

## Slide 11
The Shared-Data Bugs


The problem is due to the shared array iTemperatures.
These bugs are very difficult to find as they occur only when the interrupt occurs between the first 2 MOVE instructions, otherwise the code works fine.
11

## Slide 12
Solving The Shared-Data Problem
The problem can be solved by disabling the interrupts during the instructions that use the shared variable and re-enabling them later, e.g.:
while (TRUE)
{
disable(); ; Disable interrupts
iTemp0 = iTemperatures[0];
iTemp1 = iTemperatures[1];
enable(); ;Re-enable interrupts
...
;Remaining code same as in the previous example
...
}
12

## Slide 13
“Atomic” and “Critical Section”


A part of a program is “atomic” if it cannot be interrupted. Hence, the code between disable() and enable() above is atomic. Atomic might also be used for codes that only disable interrupts working with the same data. Hence if interrupts not associated with the temperature variable (like pressure, time etc.) are left enabled, code is still considered atomic and free of bugs.
13

## Slide 14
Shared Data Examples
Few Examples


Consider an ISR that updates iHours, iMinutes and iSeconds every second through a hardware timer interrupt. The function to calculate the time can be written as follows:
long iSecondsSinceMidnight (void)
{
long lReturnVal;
disable();
lReturnVal =
(((iHours*60) + iMinutes) * 60) + iSeconds; enable();
return (lReturnVal);
}
A problem in the above code arises when the function is called from a critical section that has disabled interrupts. The function will incorrectly enable interrupts on return.
14

## Slide 15
Data Changing in ISRs
static long int lSecondsToday;
Void interrupt vUpdateTime (void)
{
……
++lSecondsToday;
if(lSecondsToday == 60L * 60L * 24L) lSecondsToday = 0L;
……
}
Long lSecondsSinceMidnight (void)
{
long lReturn;
/* When we read the same value twice, it must be good.*/
lReturn = lSecondsToday;
while(lReturn != lSecondsToday)
lReturn = lSecondsToday;
return(lReturn);
}
15

## Slide 16
Volatile Data



However certain compilers will optimize the code. It will read lSecondsToday in one or more registers and instead of updating the value before saving it to lReturn it will read the value from the register every time instead of from memory.
Some compilers might also remove the while-loop during optimization causing the same bug with a single read.
This is prevented by declaring lSecondsToday as volatile. This warns the C compiler that the variable might change due to interrupts or other routines and not to optimize code pertaining to it.
static volatile long int
lSecondsToday;
16

## Slide 17
Interrupt Latency


Interrupt latency is the amount of time taken to respond to an interrupt.
This depends on several factors:
1.
2.
3.
4.
Longest period during which the interrupt is disabled Time taken to execute ISRs of higher priority interrupts Time taken for the microprocessor to stop the current execution, do the necessary ‘bookkeeping’ and start executing the ISR
Time taken for the ISR to save context and start executing instructions that count as a ‘response’

The third factor is measured by knowing the instruction execution times from the processor manual, when instructions are not cached.
17

## Slide 18
Minimizing Latency
 Factor 1 is affected by your SW Architecture Don’t disable interrupts too long
 Factors 2 and 4 are controlled by writing short efficient code.
Make ISRs short
 Factor 3 depends on hardware and is not under software control.
Pick a good processor
18

## Slide 19
Latency and Disabling Ints



Disabling interrupts increases interrupt latency so this period should be kept as short as possible. Consider the scenario in which two different task codes disable interrupts for 125 and 250 µs respectively.
In this case the max. time taken to start executing an ISR will be 250 µs and not 125+250 µs because ISR is started as soon as the interrupts are re- enabled in either one of the atomic sections.
19

## Slide 20
Alternatives to Disabling Interrupts


As disabling interrupts increases latency, consider alternatives in certain situations. Code on the following slide uses two array sets iTemperaturesA and
iTemperaturesB and a variable
(fTaskCodeUsingTempB) to ensure that the ISR always works with the array not being used by the task code.
20

## Slide 21
Data Sharing Example
Static int iTemperaturesA[2];
Static int iTEmperaturesB[2];
Static BOOL fTaskCodeUsingTempsB = False;
Void interrupt vRead Temperatures (void)
{
if(fTaskCodeUsingTempsB)
{
iTemperaturesA[0] = !!read in value from HW iTemperaturesA[1] = !!read in value from HW
}
Else
{
iTemperaturesB[0] = !!read in value from HW iTemperaturesB[1] = !!read in value from HW
}
}
Void main(void)
{
while(TRUE)
{
if(fTaskCodeUsingTempsB)
if(iTemperaturesB[0] != iTemperaturesB[1])
!!Set off howling alarm;
else
if(iTemperaturesA[0] != iTemperaturesA[1])
!!Set off howling alarm;
fTaskCodeUsingTempsB = !fTaskCodeUsingTempsB;
}
}
21